ATES assessment for:-

Done by: -							Date:-

|  | 1 – Simple | 2 – Challenging | 3 – Complex |
| --- | --- | --- | --- |
| Slope angle | Angles generally < 30° | Mostly low angle, isolated slopes > 35° | Variable with large % >35° |
| Slope shape | Uniform | Some convexities | Convoluted |
| Forest density | Primarily treed with some forest openings | Mixed trees and open terrain | Large expanses of open terrain. Isolated tree bands |
| Terrain traps | Minimal, some creek slopes or cut banks | Some depressions, gullies and/or overhead avalanche terrain | Many depressions, gullies. Cliffs, hidden slopes above gullies, cornices |
| Avalanche frequency (events:years) | 1:30 ≥ size 2 | 1:1 for < size 2 1:3 for ≥ size 2 | 1:1 < size 3 1:1 ≥ size 3 |
| Start zone density | Limited open terrain | Some open terrain. Isolated avalanche paths leading to valley bottom | Large expanses of open terrain. Multiple avalanche paths leading to valley bottom |
| Run-out zone characteristics | Solitary, well defined areas smooth transitions, spread deposits | Abrupt transitions or depressions with deep deposits | Multiple converging run-out zones, confined deposition area, steep tracks overhead. |
| Interaction with avalanche paths | Run-out zones only | Single path or paths with separation | Numerous and overlapping paths |
| Route options | Numerous, terrain allows multiple choices | A selection of choices of varying exposure, options to avoid avalanche paths | Limited chances to reduce exposure, avoidance not possible* |
| Exposure time | None, or limited exposure crossing run-outs only | Isolated exposure to start zones and tracks | Frequent exposure to start zones and tracks |
| Glaciation | None | Generally smooth with isolated bands of crevasses | Broken or steep sections of crevasses, icefalls or serac exposure |
| Using this scale: Any given piece of mountain terrain may have elements that will fit into multiple classes. Applying a terrain exposure rating involves considering all of the variables described above, with some default priorities. Terrain that qualifies under an italicized descriptor automatically defaults into that or a higher terrain class. Non-italicized descriptors carry less weight and will not trigger a default, but must be considered in a combination with the other factors. * Route options needs assessing in combination with Avalanche frequency. It only defaults to challenging or complex if the frequency assessment fits the challenging or complex criteria. |
| ATES classification:- Simple Challenging Complex |
| Comment:- |